## Slide 1: Implementing SIP Services
Henry Sinnreich
WorldCom
Boston, July 18, 2000
* The views expressed in this presentation may or may not represent the views of my company
Session 1: Advanced SIP Services

## Slide 2: Scalable Complexity
voice
voice
mail
voice
mail
web
voice
mail
web
presence
voice
mail
web
presence
QoS
voice
mail
web
presence
QoS
security
Telephony
Telephony
and e-mail
Integrated
voice and
data
communications
New services
Commercial
quality
e-commerce
Complexity of vertically integrated systems
Value of communications
IETF features
loss
gain

## Slide 3: New: IP Communications
Seamless integration with the web
Mobility
Unified Messaging (ex: sip message waiting)
Presence
Instant messaging using any/all media
Caller and called party preferences
3rd party call control
Mixed Internet-PSTN services
…also emulate all PSTN IN/PBX features…

## Slide 4: Presence and Instant Communications can be provided by SIP: 7 new I-Ds!
Presence
  Location: office, home, travel,…
  Call state: ready, on another call (ID),
  Willingness: available, in meeting,
  Preferred medium: text, voice, video, e-mail
  Caller preferences
  Message call waiting
Hop-on to an existing call – instant conference
Mobile phone state: online, with camp-on
Location based screening: home/work
Intercom telephony: between trading desks
Presence for any type of communications: SIP
Cannot be provided by PSTN, H.323 or MEGACO/H.248

## Slide 5: Commercial SIP and MGCP Products*
* SuperComm2000 demo

## Slide 6: Enterprise Communications Today
Reference: Teresa Hasting, VON Spring 2000
Customer
Site
Service Provider
Network
PBX
PBX
Customer
Site
Voice VPN
Voice VPN
. . .
. . .
.
.
.
.
.
.
Ent. LAN
Enterprise WAN
Ent. LAN
PSTN
Notes: The following series of slides shows an evolution of services that can be built, in incremental fashion for the business customer.
Today businesses generally carry their Voice and Data traffic on two separate networks.
Typically, there is a PSTN/PBX network, sometimes with value added network services (like VNET dialing and services).
Enterprise network is some kind of data network. Often, this has evolved to an IP-based network, running over a variety of layer 2 networks (ATM, FR, Private Line, etc), allowing the company to ubiquitously deploy data and information services and applications across the enterprise. However, ‘communications’ services (telephony) have not yet been integrated onto this network.
Access is separate, and costly, often requiring LEC FG-D for the voice traffic.
Requires separate organization and skills within the enterprise to run these networks.

## Slide 7: 1 - Enterprise Managed Network PBX-PBX Trunk Replacement
Service Provider
Network
Customer
Site
Customer
Site
Enterprise
Gateways
Ent. LAN
. . .
. . .
Service Provider
IP Net
PBX
.
.
.
PBX
.
.
.
Voice VPN
Voice VPN
Enterprise WAN
Ent. LAN
PSTN
OSS
Management
Reference: Teresa Hasting, VON Spring 2000
Notes: Many companies are beginning to move their voice traffic across their data networks. We see this over FR networks, frequently. More often enterprises are moving to VoIP. Engineering the data network to handle this traffic reliably and with good-enough quality has been some bit of an issue, but significant customers are doing this already. Moves minutes from carrier networks to private backbone.
PBXs still provide some calling features and allow off-net calling to the PSTN.
Opportunity: help customers take this step with managed service offering (as a first step).
Install VoIP gateways on the enterprise, help them engineer their network, manage dialing plans in the gateways, monitor and maintain the gateways for them.
We are working to deliver this to the field in 2Q2000. It is mostly a stepping stone to the following phases.

## Slide 8: 2 - Enterprise Managed Network with Network Routing/Dialing PLans
Customer
Site
Enterprise
Gateways
Ent. LAN
. . .
. . .
Service Provider
Network
PBX
.
.
.
PBX
.
.
.
Customer
Site
Voice VPN
Voice VPN
Enterprise WAN
Ent. LAN
PSTN
Services
Dialing
Plans
OSS
Service Provider
IP Net
Reference: Teresa Hasting, VON Spring 2000
Notes: Many companies are beginning to move their voice traffic across their data networks. We see this over FR networks, frequently. More often enterprises are moving to VoIP. Engineering the data network to handle this traffic reliably and with good-enough quality has been some bit of an issue, but significant customers are doing this already. Moves minutes from carrier networks to private backbone.
PBXs still provide some calling features and allow off-net calling to the PSTN.
Opportunity: help customers take this step with managed service offering (as a first step).
Install VoIP gateways on the enterprise, help them engineer their network, manage dialing plans in the gateways, monitor and maintain the gateways for them.
We are working to deliver this to the field in 2Q2000. It is mostly a stepping stone to the following phases.

## Slide 9: 3 - Enterprise Managed Network Can remove PBX PSTN connections
Customer
Site
Enterprise
Gateways
Ent. LAN
. . .
. . .
PBX
.
.
.
PBX
.
.
.
Customer
Site
Enterprise WAN
Ent. LAN
PSTN
Services
Dialing
Plans
OSS
Service Provider
IP Net
Shared
Network
Gateways
Reference: Teresa Hasting, VON Spring 2000
Notes: Many companies are beginning to move their voice traffic across their data networks. We see this over FR networks, frequently. More often enterprises are moving to VoIP. Engineering the data network to handle this traffic reliably and with good-enough quality has been some bit of an issue, but significant customers are doing this already. Moves minutes from carrier networks to private backbone.
PBXs still provide some calling features and allow off-net calling to the PSTN.
Opportunity: help customers take this step with managed service offering (as a first step).
Install VoIP gateways on the enterprise, help them engineer their network, manage dialing plans in the gateways, monitor and maintain the gateways for them.
We are working to deliver this to the field in 2Q2000. It is mostly a stepping stone to the following phases.

## Slide 10: 4 - Desktop Services with IP phones and devices, PBXs can be decommissioned
Reference: Teresa Hasting, VON Spring 2000
Customer
Site
Enterprise
Gateways
Ent. LAN
. . .
. . .
PBX
.
.
.
PBX
.
.
.
Customer
Site
Enterprise WAN
Ent. LAN
PSTN
Services
Dialing
Plans
OSS
Service Provider
IP Net
.
.
.
.
.
.
SIP Phones
SIP Phones
Shared
Network
Gateways
Notes: Many companies are beginning to move their voice traffic across their data networks. We see this over FR networks, frequently. More often enterprises are moving to VoIP. Engineering the data network to handle this traffic reliably and with good-enough quality has been some bit of an issue, but significant customers are doing this already. Moves minutes from carrier networks to private backbone.
PBXs still provide some calling features and allow off-net calling to the PSTN.
Opportunity: help customers take this step with managed service offering (as a first step).
Install VoIP gateways on the enterprise, help them engineer their network, manage dialing plans in the gateways, monitor and maintain the gateways for them.
We are working to deliver this to the field in 2Q2000. It is mostly a stepping stone to the following phases.

## Slide 11: 5 - Target Environment
Reference: Teresa Hasting, VON Spring 2000
Ent. LAN
. . .
. . .
Enterprise WAN
Ent. LAN
PSTN
Services
Dialing
Plans
OSS
Service Provider
IP Net
.
.
.
.
.
.
SIP Phones
SIP Phones
3rdParty
Services
Wireless
Voice &
Data
Shared
Network
Gateways
(voice
browsing
the Web)
Notes: Many companies are beginning to move their voice traffic across their data networks. We see this over FR networks, frequently. More often enterprises are moving to VoIP. Engineering the data network to handle this traffic reliably and with good-enough quality has been some bit of an issue, but significant customers are doing this already. Moves minutes from carrier networks to private backbone.
PBXs still provide some calling features and allow off-net calling to the PSTN.
Opportunity: help customers take this step with managed service offering (as a first step).
Install VoIP gateways on the enterprise, help them engineer their network, manage dialing plans in the gateways, monitor and maintain the gateways for them.
We are working to deliver this to the field in 2Q2000. It is mostly a stepping stone to the following phases.

## Slide 12: Distributed Web Customer Relations Management (CRM)
Replace voice circuit switches
Replace ACD box
Replace IVR box
Integrated PC-SIP Phone operator position
Click and connect conferencing
Integrated mail routing and management
Innovative customer support
Bigger business potential than VoIP?
Use SIP, CPL, XML

## Slide 13: SIP WG Items at the 47th IETF - 1
SIP Architecture and Functionality
  Framework for SIP Call Control Extensions
  Distributed Call State
  Event Notification in SIP
  Control of Service Context using SIP Request-URI
  Transporting User Control Information in SIP REGISTER Payloads
  SIP Server Features Negotiation
  SIP Session Timer
  Reliability for Provisional Messages
  DHCP Option for SIP Servers
  SIP Server Features
  Reliability of Provisional Responses in SIP
Services
  SIP Caller Preferences and Callee Capabilities
  Third Party Call Control in SIP
  Call Flows (Informational)
  SIP Telephony Call Flow Examples
  SIP Call Control : Transfer
  Usage of TRIP in Gateways for Exporting Phone Routes
  Distributed Multipoint Conferences using SIP
  SIP-Telephony
  Single Line Extension
http://www.greycouncil.com/sipwg/drafts

## Slide 14: SIP WG Items at the 47th IETF - 2
Infrastructure: AAA, QoS and Security
  Integration of Resource Management and SIP for IP Telephony
  Interdomain QoS, Authorization and Usage Reporting
  Getting SIP through Firewalls and NATs
  Security Group
  SIP-QoS-OSP (may find home in AAAarch)
PSTN and H.323 support
  Best Current Practice for ISUP to SIP mapping
  H.323-SIP Group
Presence and Instant Messaging
  SIP Precedence mapping to MLPP Interworking
Mobility
  SIP Mobility Support (Telcordia)
Packet Cable
  Convergence with the PacketCable DCS Spec (DCS Team)
  DCSGroup (AT&T/Cablelabs) SIP Services Architecture
  DCSGroup SIP Extensions for Caller Identity, Privacy and Operator Services
  DCSGroup SIP Extensions for supporting Distributed Call State
  DCSGroup SIP Extensions for Media Authorization
  DCSGroup SIP proxy-to-proxy extensions for supporting

## Slide 15: Early I-Ds for the 48th IETF (as of 7/17)
SIP Architecture and Functionality
  Guidelines for Authors of SIP Extensions
  SIP MIB
  SIP and SOAP
  SIP Extensions for supporting distributed call state
  SIP INFO vn. 5
  SIP INFO method for event reporting
  SIP INFO method for DTMF digit transport and collection
  SDP media alignment in SIP
  SCTP as a Transport for SIP
Services
  Emergency Call Services (911)
  A SPIRITS solution based on virtual SIP user agents
  Third party call control in SIP
  SIP message waiting
  SIP call control transfer
  SIP for the hearing disabled
Infrastructure: AAA, QoS and Security
  SIP transport of OSP token
  SIP firewall solution
PSTN and H.323 support
  H.323-SIP
  MIME media types for ISUP and QSIG objects

## Slide 16: Unified Messaging: SIP Message Waiting
Notifier -> Subscriber
SIP/2.0 200 OK
To: <sip:rohan@cisco.com>
From: <sip:rohan@cisco.com>
Date: Mon, 10 Jul 2000 17:09:36 -0700
Call-Id: 1349883@dhcp78-193.cisco.com
CSeq: 7 SUBSCRIBE
Expires: 0
Event: message-summary
Content-Type: text/xml
Content-Length: 231
<MESSAGE_SUMMARY>
<MAILBOX_IN>
<NAME>Inbox</NAME>
<VOICEMAIL>
<UNTOUCHED>1</UNTOUCHED>
<READ>2</READ>
<ANSWERED urgent="1">1</ANSWERED>
<DELETED>2</DELETED>
</VOICEMAIL>
</MAILBOX_IN>
</MESSAGE_SUMMARY>
Text to Voice
Inbox
Your have the following messages:
one new message
two read messages
one answered urgent message
two deleted messages
Reference: Rohan Mahy, Ilya Slain/Cisco

## Slide 17: A SPIRITS solution based on virtual SIP user agents
Call originating
  Call barring
  Speed dialing
  VPN
  Number portability
Call terminating
  Conditional redirect
  Call filtering (user pref’s)
  Internet call waiting
  Caller ID
Call progress informative
  Mobile presence,
  busy,
  reject
SPIRITS
Server
SPIRITS
SIP Proxy
SPIRITS
SIP Client
Voice net service function
Reference: S. Björkner, S. Nyckelgard/HotSip, Telia

## Slide 18: IMPP WG: SIP Integrated I-Ds *
A Model for Presence and Instant Messaging **
SIP Extensions for Presence
SIP Extensions for Presence Authorization
SIP Extensions for Instant Messaging
A Data Format for Presence Using XML
A Lightweight Presence Information Format (LPIDF)
An XML Format for Presence Buddy Lists
An XML Based Format for Watcher Information
* Co-authored by Cisco, Columbia U., DynamicSoft and Microsoft
** Presented at the 47th IETF
Personal notes in no particular order

## Slide 19: IMPP WG: Non-SIP Integrated I-Ds
Presence Information Data Format for IMPP *
Transport Protocol for Presence Information/ Instant Messaging *
Security Framework for Instant Messaging and Presence Protocol *
Simple Instant Messaging and Presence 1.1 Protocol
Security in the Instant Message and Presence Protocols
Sametime (TM) Community - Client Protocol
Instant Messaging / Presence Architecture
Privacy-enhanced Presence Protocol (PePP)
Presence Information Data Format
An Architecture and Protocol for Presence and Instant Messaging
Transport Protocol for Presence Information/ Instant Messaging
Instant Messaging / Presence Protocol Design Issues
Proposed Design Decisions for IMPP
Security Framework for Instant Messaging and Presence Protocol
Interoperability with America Online's Instant Messaging Services
* Presented at the 47th IETF
Personal notes in no particular order

## Slide 20: Conclusion
SIP Develops!