## Slide 1: SIP Telephony Services
Henry Sinnreich
MCI WorldCom
henry.sinnreich@wcom.com
Evolution of Internet Standards:

## Slide 2: Summary
Why use IETF and W3C standards?
Relevant IETF working groups
Services: PSTN - Internet and beyond
Services: IP VNET and IP Centrex
SIP for presence, instant messaging and voice
SIP clients
Gap analysis for IP telephony
Call Setup: H.323, MGCP and SIP/SDP
Billing Model for SIP and gateway services
PSTN and SIP-XML billing models

## Slide 3: Why Use IETF and W3C Standards
1998
1999
2000
2001
2002
2003
2004
2005
Internet
Frame Relay
ATM
Private Line
Voice
IETF/W3C
standards
ITU, other
standards
My estimate of traffic growth from public data
Practically all new services, new revenue and investments will go to the Internet, based on Internet and W3C standards
Notes: Everybody can have the same claim to speak to God and predict the future: According to professional forecasts we were to live now in the “Era of Broadband ISDN” (ITU Documents) and nobody predicted the Internet.
Growth information was taken from published market projections for predicted year over year growth of each service. It also shows expected legacy network growth if we follow the perceived market trends.
Chart Data
1998 1999 2000 2001 2002 2003 2004 2005
Voice 3000 3500 3500 3500 3500 3500 3000 3000
Private Line 4000 4200 4800 4800 4800 4600 4800 4000
ATM 500 1000 2000 2700 4800 7000 7700 10500
Frame Relay 500 600 700 1000 900 900 900 800
Internet (**) 1500 3000 6000 12000 24000 48000 96000 192000
(**) - 2x - year

## Slide 4: Relevant IETF Working Groups
AVT: RTP
MMUSIC: SDP, SIP and extensions
IPTEL: CPL and GLP
PINT (PIN): PSTN-Internet services
MEGACO: Media gateway control
SIGTRAN: Telephony signaling transport
http://ietf.org/html.charters/wg-dir.html
See also http://w3c.org/

## Slide 5: SIP Services: PSTN - Internet Interaction and Beyond
SCP
PSTN
PSTN-IP end-to-end
All IN services
  CS-1
  CS-2
Beyond IN services
New PIN services
Presence
Mobility
End-to end control on IP network
Signaling GWY
GWY
Control
Media
GWY
SS7
PCM
RTP
MGCP, MEGACO
SIGTRAN
SIP
Network Gateway
SIP
Server
Network
GWY
Internet

## Slide 6: SIP Services: IP VNET and IP Centrex
IP VNET
IP trunking
PSTN bypass
Private numbering plan
Features in PBX
SIP call routing
IP Centrex
Virtual SIP PBX
PSTN bypass
Private numbering plan
SIP call routing
SIP
Server
PBX
PBX
Enterprise
GWY
Network
GWY
IP
PSTN
PSTN
Enterprise
GWY
Network
GWY
PSTN
IP
PSTN
Network
GWY
SIP
Server
Network
GWY
SIP Ethernet phones
Proprietary PBX phones

## Slide 7: SIP Phones and Adaptors
SIP phones courtesy of 3Com
Mediatrix Phone Adaptor
SIP phone courtesy Columbia University
Etherset phone courtesy Nortel

## Slide 8: SIP for Presence, Instant Messaging and Voice
SUBSCRIBER
SERVER
SERVER
PUBLISHER
DB & POLICY
A – subscription
B – access control
C – notification
D – publishing
E – database and policy
A
A
B
D
C
C
E
USER
USER
Presence systems and voice call setup are nearly identical
Add two methods to SIP:
SUBSCRIBE
NOTIFY
Presence and telephony integration
Reference: SIP for Presence (I-D)
*1999 Ericsson
Presence in proprietary commercial systems got the interest of the IETF

## Slide 9: Gap Analysis for IP Telephony Single IETF Standard implementations (without options) wanted for:
Technology
QoS on slow links
Firewalls
Header is 40 bytes
Modeling
Fax
PSTN-Internet services
Clearing house
Gateway location
Applications
Announcements
Conferences
Voice mail
Messaging
XML/CPL
IVR
Web support centers (more than phone call centers)
Service Systems
Web ordering
Web fulfillment
Web support center
Web payments
Directory driven

## Slide 10: Call Setup: H.323, MGCP and SIP/SDP
Sparse vendor support
(mostly top tier vendors)
Central control conflicts with:
User control of services,
Outsourcing,
Mobility,
Inter-domain operation
No new services
Legacy of ISDN
Divergence from IP apps
No real interoperability
Patents
New services beyond voice
Integration of voice & IP
Same IP network
Lightweight software
Easy service creation
User control
Presence
Mobility
Inter-domain
Replaces H.323 gatekeeper model
Absorbs the complexity of PSTN at the edge of the Internet
Useful for controlling many gateways in IP CO
Like the bus of a CO switch
Will MEGACO be worse?
Vendor support
SIP/SDP: Build on it
MGCP: Use it
H.323: Support it
All IP telephony standards are still under under development
(too many chefs in the kitchen?)

## Slide 11: Billing Model for SIP and Gateway Services
SIP client
Phone
AAA and
Policy
Server
Legacy
Data Base
SIP server
Policy client
IP Tel
Gateway
PSTN
SIP
ISDN or SS7
AAA and
Policy messages
SIP CGI
SIP policy events:
INVITE
ACK
CANCEL
BYE
SIP
PDP
PEP
SIP call requires user authentication
QoS request granted by policy server
Legacy databases access using SIP CGI
Separate charging and call logging possible for
SIP services
Gateway services

## Slide 12: PSTN and SIP-XML Billing Models
client
client
ISP Policy
Backbone Policy
SIP
Srv.
ISP AAA
SIP
Srv.
SIP
Srv.
SIP
Srv.
CALLER
CALLED
Caller gets real time pricing and payment information
ISP
ISP
Backbone
ISP
XML
Records
Intra-Domain
XML
Records
ISP
XML
Records
PSTN LD call billing model
SIP-XML Internet call billing model
phone
phone
IEC
SW
LEC Billing
IEC Billing
LEC Billing
LEC
SW
LEC
SW
CALLER
CALLED
Caller gets
bill from LEC
Local
Local
Long Distance
Settlement
Settlement
IEC
SW
IEC
SW
LEC
SW
LEC
SW

## Slide 13: References
“Internet Telephony – An Overview” by Jiri Kuthan
http://www.fokus.gmd.de/research/cc/glone/projects/ipt/
May 1999 IEEE Network/Internet Computing special issue on IP telephony
Henning Schulzrinne “SIP Home Page”
http://www.cs.columbia.edu/~hgs/sip/
SIP for Presence by J. Rosenberg and H. Schulzrinne http://ietf.org/internet-drafts/draft-rosenberg-sip-pip-00.txt
Book on “Internetworking Multimedia” by Jon Crowcroft, Mark Handley, Ian Wakeman, UCL Press, to be published in September 1999 by Morgan Kaufman (USA) and Taylor Francis (UK)